## Slide 1
Slide 1 — IDEA TITLE & TEAM DETAILS
AgniRakshak: Distributed Edge-AI Wildfire Early Detection Network
• Theme / Track: Open Innovation
• Idea Title: AgniRakshak (अग्निरक्षक)
• Tagline: Detect Early. Alert Faster. Prevent Wildfires.
• Team Name: Hell Fire Club
• Institution: Manipal University Jaipur (IIC 3.0)
• Core Value Prop: Sub-minute wildfire ignition detection combining solar-powered IoT micro-climate sensor fusion with temporal derivative AI classification (dT/dt, dCO/dt).

## Slide 2
Slide 2 — PROBLEM STATEMENT
Critical Latency & Failure of Existing Monitoring Methods
• Satellite & Camera Latency: Satellites have 1-3 hour pass delays; by detection time, small ignitions escalate into catastrophic mega-fires.
• Remote Forest Blindspots: Deep wildlands lack power grid infrastructure and continuous physical human surveillance.
• Single-Threshold Failure: Conventional static temperature alarms produce false triggers from hot ambient weather or fail in outdoor wind.
• Severe Consequences: Massive ecological destruction, megatons of unmitigated CO2 emissions, and loss of life & property.

## Slide 3
Slide 3 — PROPOSED SOLUTION
Multi-Sensor Edge-AI Sensor Fusion Platform
• Distributed Sensor Nodes: Deploy autonomous micro-climate nodes capturing Temp, Humidity, CO, Smoke, and Barometric Pressure.
• Temporal Derivative Engine: Computes rate-of-change metrics (dT/dt, dCO/dt) to detect chemical ignition before visible smoke/flames.
• Hybrid AI Classifier: Scikit-Learn Random Forest model + deterministic heuristic safety rules classify risk: NORMAL, WARNING, HIGH RISK.
• GPS & Sub-Minute Alerts: Instant geolocation tagging via LoRa / Wi-Fi mesh dispatches responders within 60 seconds.

## Slide 4
Slide 4 — INNOVATION & UNIQUENESS
Why AgniRakshak Outperforms Traditional Fire Alarms
• Feature Fusion vs Static Thresholds: Combines multi-parameter temporal trends instead of single threshold triggers (e.g. Temp > X).
• Sub-Minute Detection Speed: Local edge detection triggers instant alarm buzzer and cloud dashboard alerts.
• Physics-Based Calibration: Polynomial bivariate temperature & humidity correction K(T, H) eliminates sensor drift false alarms.
• Ultra-Low Cost & Off-Grid: Complete node BOM < $35 with solar MPPT harvesting and 19-day dark autonomy.

## Slide 5
Slide 5 — TECHNICAL APPROACH & ARCHITECTURE
Hardware, Firmware, and Cloud AI Stack
• Hardware Layer: ESP32 DevKit MCU + Bosch BME280 + MQ-7 CO (5V/1.4V cycle) + MQ-2 Smoke + NEO-6M GPS.
• Firmware Architecture: FreeRTOS dual-core task scheduling (Core 0: Sensor conditioning; Core 1: OLED, Alerts, Wi-Fi TX).
• AI & Software Stack: Python Streamlit Web Dashboard + Scikit-Learn Random Forest Model + Folium Geospatial Map.
• Power Management: 5W Monocrystalline Solar + CN3791 MPPT + 6000mAh LiFePO4 battery (< 13mA avg draw).

## Slide 6
Slide 6 — PROTOTYPE & WORKING DEMONSTRATION
Full-Stack Implementation Deliverables
• Interactive Streamlit Dashboard: Real-time web monitoring interface featuring live risk gauges, Folium map, and Plotly charts.
• Live Scenario Simulator: Test controls for 4 scenarios: Normal Ambient, Hot & Dry Weather, Smoldering Fire, Active Wildfire.
• ESP32 Firmware Code: Production C++/Arduino sketch with FreeRTOS, OLED status display, active buzzer, and JSON HTTP client.
• Trained ML Engine: Persisted Scikit-Learn Random Forest classifier model artifacts (wildfire_model.pkl).

## Slide 7
Slide 7 — FEASIBILITY & VIABILITY
Economic & Power System Autonomy
• Node Cost (< $35): ESP32 ($4.50), BME280 ($3.20), MQ-7/MQ-2 ($4.80), GPS & OLED ($6.50), Solar MPPT & Battery ($12.00).
• 5-Min Periodic Duty Cycle: Consumes 12.63 mA average current at 3.3V (0.041 W power consumption).
• 19-Day Dark Autonomy: 6000 mAh LiFePO4 battery runs over 19 days without solar replenishment during dense smoke plumes.
• IP65 Polycarbonate Enclosure: Dual-compartment sealed electronics housing with louvered 45° rain protection sensing chamber.

## Slide 8
Slide 8 — IMPACT & FUTURE ROADMAP
Environmental Preservation & Scalability
• Ecological Impact: Protects forest biodiversity, wildlife habitats, and reduces unmitigated carbon emissions.
• Economic Protection: Prevents multi-million dollar timber, agricultural, and community infrastructure losses.
• LoRa Mesh Scaling: Expand nodes across thousands of forest hectares using sub-GHz LoRa RF mesh networking.
• Future Integration: Combine ground IoT sensor mesh telemetry with autonomous drone verification and satellite maps.

## Slide 9
Slide 9 — CONCLUSION & SUMMARY VISION
Detect Early. Alert Faster. Prevent Wildfires.
• Core Vision: Deploy a continuous, autonomous network of edge-AI nodes across vulnerable forest ecosystems.
• System Workflow: MONITOR -> DETECT -> ANALYZE -> ALERT -> ACT
• Competitive Advantage: Open Innovation track choice preserves Round 1 solution for offline physical presentation at MUJ.
• Final Tagline: AI + IoT + Early Sensor Fusion = A Smarter Approach to Wildfire Prevention.